## Slide 1
16881A0368

## Slide 2
ANALYSIS OF WIND TURBINE BLADE
SOFTWARE USED :
ANSYS WORKBENCH
MATERIAL USED :
ALUMINIUM ALLOY

## Slide 3
WIND TURBINE BLADE

## Slide 4
ANALYSIS :
CASE 1 :
Perform Transient Structural Analysis with linked modal Analysis with the following inputs :
Max Pressure : 101325 Pa
Apply Pressure on the blade and constraint the end locations ( i.e, holes)
Perform the Analysis for 100 sec.
MODAL ANALYSIS :
Perform the modal analysis with pre-stress condition as static structural analysis :
Number of modes to find : 6
OUTPUT :
Stress (Von-Mises)
Deformation
Strain
Factor of safety.

## Slide 5
CASE 2:
HARMONIC ANALYSIS :(MODE SUPERPOSITION)
Max Frequency : 300 Hz
Max Pressure : 101325 Pa
Apply pressure on the blade and constraint the end location( i.e, holes)
OUTPUT:
Displacement(Vs)Frequency.
CASE 3:
FATIGUE ANALYSIS :
Using the above conditions perform fatigue analysis
OUTPUT :
Life
Damage.

## Slide 6
DETAILS OF MESH
Mesh size : Max element size-34 mm
Min element size-19 mm
Element order : linear
Element size : default
Mesh type : 3-D,Tetra-meshing
Element shape : Tetra hedron
NODES : 4024
ELEMENTS : 15287

## Slide 7
MESH

## Slide 13
LINKING STRUCTURAL WITH MODAL

## Slide 26: As I have calculated the deformation,stress,strain,factor of safety with aluminium and the same is shown as below
 | DEFORMATION | STRESS | STRAIN | SAFETY FACTOR
TRANSIENT | 0.046712 | 1.385 | 7.73732e-6 | 15
DEFORMATION | 1 | 2 | 3 | 4 | 5 | 6
MODAL ANALYSIS | 4.0685 | 4.6018 | 7.2081 | 8.086 | 7.0641 | 8.0541
 | LIFE | DAMAGE
FATIQUE ANALYSIS | 1e6 | 1000

## Slide 27: CONCLUSION
In this project I worked on wind mill turbine blade and analysis is done in ansys software . Analysis like transient ,modal , harmonic and fatique were performed to find stress ,strain , factor of safety and deformation , etc.
From the observation regarding the values obtained I can conclude that Aluminium Alloy can be best suited for wind turbine blade and it has given best results.

## Slide 28: Thank you
.